## Slide 1
Neo Fang, 2/19/2020
RISCV random instruction generator
Notes: <number>

## Slide 2
Agenda
NV RISCV random generator introduction
Google RISCV random generator introduction
Comparison

## Slide 3
Instruction random challenge
Easy part (In control)
  ALU/IMD and other instructions like FENCE, SFENCE, ECALL …
  Known PC result (pc+4, pc+2 or trap) without knowing GPR/CSR value
Difficult part (Out of control)
  Branch, LSU and CSR instructions
  PC result depends on GPR/CSR value (branch taken/no taken, branch target, trap/no trap)
  Backward branch may cause dead loop
  Store could modify instruction/data region and affect other instructions

## Slide 4
Common solution
la x10, base_addr
lw x11, x10, 20
Fixed LSU sequence
branch
target
Only forward branch
Random
sequence
Direct
sequence
Backward branch
CSR changing
Move from random to direct
la x10, base_addr
JALR x1, x10, 20
Fixed JALR sequence

## Slide 5
Our solution
rand_inst x10 …
lw x11, x10, 20
Random LSU sequence
branch
target
Random forward/backward branch
With dead lock handling
Random
sequence
Direct
sequence
Backward branch
CSR changing
Keep in random sequence
rand_inst x10 …
JALR x1, x10, 20
Random JALR sequence
target
GPR=…
CSR=…
Calculate
instruction
Notes: <number>

## Slide 6
Generator flow
Test initialization for CSR, trap handler, mpu, pmp and etc
Generation loop start. Set current pc with boot start pc
Calculate current instruction. Get next pc and other GPR/CSR result
Generate random instruction with constraint and insert at next pc
Loop until specified amount of instructions are generated
Necessary handling to make sure generated sequence is valid
CSR random
branch random
lsu random

## Slide 7
Generator flow
New pc pa?
Begin loop
Exit loop
Instruction decode
Calculate current instruction
Store bin code
Check override
Check dead lock
Check store fault address
Check next pc not in reserved region
Gen one inst
Next pc existed?
Check exit pc valid
Insert inst for unexecuted addr
enough?
Y
N
N
Y
N
Y
pc advance, gen next instruction
Check allowed insert bytes
Notes: <number>

## Slide 8
Add new instructions in generator
Update calculate_op() to include new instruction calculation
Update gen_inst() to generate new instruction with constraint
Other update for internal handling, this depends on instruction feature

## Slide 9
Add ALU instruction
New pc pa?
Begin loop
Exit loop
Instruction decode
Calculate current instruction
Store bin code
Check override
Check dead lock
Check store fault address
Check next pc not in reserved region
Gen one inst
Next pc existed?
Check exit pc valid
Insert inst for unexecuted addr
enough?
Y
N
N
Y
N
Y
pc advance, gen next instruction
Check allowed insert bytes
Notes: <number>

## Slide 10
Add LSU instruction
New pc pa?
Begin loop
Exit loop
Instruction decode
Calculate current instruction
Store bin code
Check override
Check dead lock
Check store fault address
Check next pc not in reserved region
Gen one inst
Next pc existed?
Check exit pc valid
Insert inst for unexecuted addr
enough?
Y
N
N
Y
N
Y
pc advance, gen next instruction
Check allowed insert bytes
Notes: <number>

## Slide 11
Add RVC instruction
New pc pa?
Begin loop
Exit loop
Instruction decode
Calculate current instruction
Store bin code
Check override
Check dead lock
Check store fault address
Check next pc not in reserved region
Gen one inst
Next pc existed?
Check exit pc valid
Insert inst for unexecuted addr
enough?
Y
N
N
Y
N
Y
pc advance, gen next instruction
Check allowed insert bytes
Notes: <number>

## Slide 12
TB environment
UVM random instruction generator
RISCV DUT
UVM sequence
UVM dummy sequencer
Memory model
CMOD
On the fly compare
backdoor
write
HEX
optional

## Slide 13
Google TB environment

## Slide 14
Google generator flow

## Slide 15
Main/sub program generation
……
……
……
……
……
……
directed
instruction
stream
queue
B
B
B
Generate main random stream
with no load/store, configurable forward branch
Put directed stream into queue with configured ratio
Mix directed instruction stream into main random stream
Assign forward branch target
Notes: <number>

## Slide 16
Load/store instruction generation

## Slide 17
Branch instruction generation

## Slide 18
Call stack
Randomly generate call stack tree structure
to avoid loop function call
main
sub1
sub2
sub3
sub4
sub5
sub6
sub7
Level 0
Level 1
Level 2
Level 3
la rd0, jump_target_label
addi rd1, offset, rd0
jalr rd, offset, rd1
Generate directed jump sequence
to jump to specified target
Insert jump sequence into program stream
for program call connection
jump seq

## Slide 19
Comparison
 | NV RISCV generator | Google RISCV generator
Implementation | UVM based | UVM based
Output format | UVM sequence(optional HEX) | ASM file
Branch random | Both in random sequence | Forward random, backward in directed sequence
LSU random | Random | Directed sequence
CSR random | Dynamically changing | Not change
Exception | All kinds of exception | Part exception
Simulation performance | Need to improve | Fast
Global configuration | Separate control | Central control
Configurable target | No | Yes

## Slide 20
Notes: <number>