## Slide 1: RISC-V CHERI Proposal
CHERI
  Capability Hardware Enhanced RISC Instructions
  The name is not very helpful and is pronounced «cherry»
It’s the result of 10 years of research by Cambridge Uni, UK
https://www.cl.cam.ac.uk/research/security/ctsrd/cheri/
There is a v8 spec, LLVM toolchain, QEMU, FreeBSD port, and some unusal RTL implementations available.
There’s a MIPS (the original), ARM and RISC-V version
  ARM has the Morello platform which has no traction at the moment
It’s about memory safety, mainly preventing buffer overflow attacks and dereferencing corrupted pointers.
  It has nothing to do with fault detection or side-channels.

## Slide 2: RISC-V CHERI Proposal
The basic technology is that every pointer becomes a capability with encoded bounds, representable range, object type (otype) and permission
A capability can only be derived from another which has more (or the same) permissions, it can never add more permissions.
The PC is a capability (PCC), so all execution is bounds checked
Load/stores can either reference the Default Data Capability, or a specific capability from the register file

## Slide 3: RISC-V CHERI Proposal
When a task is invoked, pass one or more capabilities to it, which all future capabilities are derived from, so the task can never access outside its allocated space.
Object type (otype) can be used to bind instruction/data capabilities together
Capabilities can be sealed, so they can’t be modified, unless unsealed by a capability with the correct authority
And many more similar features...

## Slide 4: OpenHW core based upon CHERI
Huawei are considering a proposal to make a new OpenHW Group core implementing CHERI
Huawei are the first major company to show real interest in CHERI
I’m currently documenting the microarchitecture, and will distribute the documentation when complete
By deviating from the publish spec, but by using existing compiler options (-cheri-uintcap=address) the implementation is greatly simplified
Main overhead is much larger / longer execution logic and all registers become 65-bit, as every register is a capability.

## Slide 5: OpenHW core based upon CHERI
The CHERI v9 spec is overdue, including compressed encodings, so will be much more usable than v8 which has a big code-size problem
The idea is to have a collaboration between Huawei, OpenHW Group and ETH Zurich Uni to do the work
In Q1 2022 Huawei will decide whether to propose the project