## Slide 1: Proposal for a CV32E20 “Tiny-FPU”
Joe Circello,
NXP Semiconductors
December 13, 2021

## Slide 2: CV32E20F
Concept of optional Floating-Point Unit as follow-on to E20
Driven by compute-intensive applications moving to “edge”
  Requires a “size-appropriate” FPU implementation
    Integer CV32E20 synthesis target for minimal configuration is ~20 Kgates
    Estimated size target for “Tiny32” extension is ~10 Kgates
      Supports the Zfinx extension to share a single regfile for both int and FP data
  Limited to single-precision support; Tiny-FPU !=, << FPnew
    Supports the RISC-V RV32F ISA extensions except for FDIV.S + FSQRT.S
    FDIV.S + FSQRT.S performed via integer emulation to minimize gate count
Concept from original May 2021 ISCAS paper by ETH-Zurich

## Slide 3: Tiny32 Details
Chart: Relative Tiny32 Performance vs Int Emulation
| knn | ReLU | con2d | fann-fp | axpy
%FP | 7.6 | 14.1 | 19.1 | 21 | 34.4
RelPerf | 4.1304 | 3.18 | 13.7914 | 10.4117 | 14.9589
Chart: Relative Tiny32 Energy Consumption vs Int Emulation
| knn | ReLU | con2d | fann-fp | axpy
FractionFP | 0.076 | 0.141 | 0.191 | 0.21 | 0.344
RelEnergy | 0.36283 | 0.44767 | 0.11475 | 0.15934 | 0.10149
Tiny32 Execution Time Latency [cycles] |  | 
fadd | 10-13 | 
fsub | 10-13 | 
fmul | 18 | 
fmadd | 21-24 | 
fcvt | 9 | 
f{eq,le,lt} | 2 | 
https://ieeexplore.ieee.org/abstract/document/9401149

## Slide 4
Thank you!