## Slide 1
Overview
Predictable & High-Performance RISC-V Multicore Framework

## Slide 2
Predictable & High-Performance RISC-V Multicore Framework
2
State-of-the-art (OpenPiton):
  + Originally designed for scalable many-core platforms
  - Trades some average performance for predictability
  - Lacks predictable performance
Examples:
  Directory-based MESI:
    A minimum of three hops per coherence request
  Distributed L2:
    Different latencies whether you are accessing your tile or others
    And also how many “tiles” you need to traverse.
Notes: 2

## Slide 3
Why Predictable Performance?
3
A mandate for functional safety
Safety-Critical Systems
ISO26262
EN 50129
IEC 62304
IEC EN 61508
Notes: 3

## Slide 4
Predictable & High-Performance RISC-V Multicore Framework
4
(1) Predictable Interconnect
(2) A predictable shared L2
(3) Snooping Coherence
(4) Predictable MC to high-performance DDR4
Goal:
  A predictable and high-performance multi-core RISC-V Infrastructure
Notes: 4

## Slide 5
5
Duetto: Dual-Mode Arbitration
HPA arbitrates among requests generated by requestors and sends commands to the hw resource
Request Queues
Requestors
(cores, GPU, accelerators, DMA…)
HPA
Resource
(cache, memory, interc. …)
Notes: 5

## Slide 6
6
Duetto: Dual-Mode Arbitration
We add a RTA that runs in parallel with the HPA
A monitor provides latency guarantees to requestors
  Desired latency requirements can be set for each requestor / type of request (CONFIGURABILITY)
  If the system is not heavily loaded, use the HPA output
  If the system is pathologically overloaded and latency guarantees could be missed (extremely rare), switch to the RTA
Request Queues
HPA
RTA
Monitor
Resource
(cache, memory, interc. …)
Requestors
(cores, GPU, accelerators, DMA…)
Notes: 6

## Slide 7
7
Duetto: Dual-Mode Arbitration
Almost no change required for the HPA
  The model works as an add-on functionality to an existing arbiter/resource (INTEGRATABILITY)
  If real-time guarantees are not needed, we can disable the RTA/monitor and the system will behave as the original one
  The RTA/monitor require some area, but vast majority of power is consumed by the resource
Request Queues
HPA
RTA
Monitor
Resource
(cache, memory, interc. …)
Requestors
(cores, GPU, accelerators, DMA…)
Notes: 7

## Slide 8
Backup Slides
Notes: 8

## Slide 9
9
Duetto: Applying to Different Memory Resources
Two resources:
  Cache coherent interconnect between private L1 and shared L2
  DRAM main memory
For each resource:
  Architectural Simulation results (current progress)
  Plan for FPGA implementation
Notes: 9

## Slide 10
10
Duetto Resource 1: Caches
Notes: 10

## Slide 11
11
Duetto Resource 2: DRAM
Notes: 11

## Slide 12
12
Duetto Resource 2: DRAM
Notes: 12

## Slide 13
13
Duetto Architectural Simulation Results
HPA
Duo$
RTA
RTA provides latencies well below the bound…
HPA shows large latency spikes
Latencies are now very close to the bound…
Resource 1: Coherent Interconnect, private L1s and bankized shared L2
Notes: 13

## Slide 14
14
Duetto Architectural Simulation Results
Resource 1: Coherent Interconnect, private L1s and bankized shared L2
>4x performance over state-of-the-art predictable coherence solution
Near-COTS performance with Duetto
Configurable deadline helps in latency vs performance trade-off
Notes: 14

## Slide 15
15
Duetto Architectural Simulation Results
Resource 2: DRAM
  8 requestors - cores running memory-intensive benchmarks - accessing the same device
  Cycle-accurate simulation using our MCsim memory controller simulation framework [1]
  Cache and bank-level partitioning for improved isolation [2]
  HPA uses standard FR-FCFS arbitration
… with only 3% average IPC reduction
HPA
Dual Mode
RTA
Notes: 15